## Slide 1: A Sequential Abstraction for Data-parallelism in Hardware Accelerators
Akash Gaonkar -- 05/2021

## Slide 2: Today’s applications use data-parallel operations
Image Processing
Machine Learning
Natural Language Processing (NLP)
Demand for efficiency => custom hardware (called accelerators)
e.g., Gaussian Blur
e.g., Max-pooling
e.g., Part-of-speech Tagging
Notes: In today’s society, we are increasingly needing to perform data-parallel operations, for various applications, including image processing, machine learning, and natural language processing (NLP).
In machine learning in particular, ever-larger models and datasets require operations to be as efficient as possible, leading to design of custom hardware (called accelerators) optimized for machine learning.

## Slide 3: Compilation to Hardware Accelerators
General purpose
NVDLA
FlexASR
HLSCNN
VTA
Application specific
Applications provided in different DSLs
Heterogeneous hardware backends
Executable/ runtime w/HW
; CPU instructions
CMP r0, r1
SUBGT r0, r0, r1
BNE loop
; Access accel 1 (MMIO)
STR r2, 0xffff0000
LDR r3, 0xffff0010
; Access accel 2 (MMIO)
STR r4, 0xffff0100
LDR r5, 0xffff0110
; CPU instructions
MOV r3, r2
SUBGT r0, r0, r1
B lr
?
huge gap!
Compiler IR (e.g. Relay IRModule)
No semantics for MMIO load/stores
Granularity mismatch
Custom numerics + memory
Notes: This gap is the target of the Princeton ILA group (led by Sharad Malik). Emphasize these are loads and stores with meaning and side-effects (MMIO instructions). Know 3 challenges mentioned in CASES paper.

## Slide 4: Instruction Level Abstraction (ILA)
General purpose
NVDLA
FlexASR
HLSCNN
VTA
Application specific
Applications provided in different DSLs
Heterogeneous hardware backends
Executable/ runtime w/HW
; CPU instructions
CMP r0, r1
SUBGT r0, r0, r1
BNE loop
; Access accel 1 (MMIO)
STR r2, 0xffff0000
LDR r3, 0xffff0010
; Access accel 2 (MMIO)
STR r4, 0xffff0100
LDR r5, 0xffff0110
; CPU instructions
MOV r3, r2
SUBGT r0, r0, r1
B lr
Instruction Level Abstraction (ILA) model
Instructions are commands at the MMIO interface of accelerators
Verified lifting of hardware operations
Compiler IR (e.g. Relay IRModule)
Huang, Bo-Yuan, et al. "ILAng: a modeling and verification platform for SoCs using instruction-level abstractions." International Conference on Tools and Algorithms for the Construction and Analysis of Systems. Springer, Cham, 2019.

## Slide 5: Instruction Level Abstraction (ILA)
General purpose
NVDLA
FlexASR
HLSCNN
VTA
Application specific
Applications provided in different DSLs
Heterogeneous hardware backends
Executable/ runtime w/HW
; CPU instructions
CMP r0, r1
SUBGT r0, r0, r1
BNE loop
; Access accel 1 (MMIO)
STR r2, 0xffff0000
LDR r3, 0xffff0010
; Access accel 2 (MMIO)
STR r4, 0xffff0100
LDR r5, 0xffff0110
; CPU instructions
MOV r3, r2
SUBGT r0, r0, r1
B lr
Compiler IR (e.g. Relay IRModule)
FlexASR func A:
instr. 1 (STR r2, 0xffff0000)
instr. 2 (LDR r3, 0xffff0010)
FlexASR func B:
instr. 3 (STR r2, 0xffffaa00)
instr. 4 (LDR r3, 0xffffaabb)
NVDLA func C:
instr. 5 (STR r4, 0xffff0100)
instr. 6 (LDR r5, 0xffff0110)
Relay-to-HW mapping via ILA models
I extend the ILA methodology to model hardware data-parallelism.

## Slide 6: Outline
Background: Instruction Level Abstraction (ILA)
SIMD (Single Instruction, Multiple Data) Instructions
Nested SIMD Instructions, SIMD Transformations
Key Points
Related Work
Future Work

## Slide 7: Addressing the Specification Gap
Lessons from Processor
Instruction Set Architecture (ISA)
ISA .
HW Abstraction
Software view of hardware
Defines semantics for SW interactions with HW
Enables SW verification
HW Specification
Specification for HW implementation
Enables implementation verification
Enables HW upgrades
ISA
Specifies visible state
  - abstracts details
Modular specification
  - set of instructions
, ILA
, ILA
ILA: Instruction-Level Abstractions
7
Slide Credit: Sharad Malik
Notes: Say ILA from Sharad Malik’s group “viewing upwards”, “viewing downwards”, (note to self: visible and persistent state – e.g. pipeline registers are not visible state)

## Slide 8: Background: Instruction Level Abstraction (ILA)
 | is a set of architectural state variables
 | is an initial assignment to
 | is a set of input variables
 | checks if an input is valid, acts a trigger for this ILA
 | is a decode function returning true if the th “instruction”, , can be executed
 | is a transition function that gives the state after the th instruction is executed
 | is a set of architectural state variables
 | is a set of input variables
 | checks if an input is valid, acts a trigger for this ILA
 | is a set of architectural state variables
 | is an initial assignment to
 | is a set of input variables
 | checks if an input is valid, acts a trigger for this ILA
 | is a set of architectural state variables
 | is a set of input variables
 | checks if an input is valid, acts a trigger for this ILA
 | is a set of architectural state variables
 | is an initial assignment to
 | is a set of input variables
 | is a set of architectural state variables
 | is a set of input variables
An ILA is a tuple where
Modified from Huang et al. TODAES’18: elided instruction fetching.
A variable or has type , Type = Bool | Bitvector(nbits) | Memory(databits, addrbits)
Likewise, the expressions used in use the same type system.
Notes: If hierarchy needed, mention in the last bullet, “ILA also supports hierarchy”
To explain: ILAs model a piece of hardware as a labeled state transition system. On types: note that these are traditional types for hardware models, which have never needed to describe operations on large complex pieces of data – that is until accelerators, and data-parallel accelerators in particular, started including somewhat custom representations of vectors and matrices with added complications like tiling.

## Slide 9: Example ILA for an AES Accelerator
Write, 0xff00, 0x1 | START_ENCRYPT
Write, 0xff02,data | WRITE_ADDRESS
Write, 0xff04,data | WRITE_LENGTH
Write, 0xff10,data | WRITE_KEY
Write, 0xff20,data | WRITE_COUNTER
Read, 0xff01 | GET_STATUS
Read, 0xff02 | READ_ADDRRESS
Read, 0xff04 | READ_LENGTH
Visible State
Interface
Length
Instructions Interface Commands
Key
Counter
Status
Address
Interconnect
Instruction | WRITE_ADDRESS
Decode, | 
Update, | 
Instruction | WRITE_ADDRESS
AES Block Encryption
Specifies visible state
  - architectural register
  - memory
Modular specification
  - set of instructions
Instruction specification
  - update to architectural states
Notes: Can note that START_ENCRYPT is a special MMIO write, note that many instructions are for config. Can use Tau[i] to point out Address is a state variable and cmd_data is an input

## Slide 10: Key themes in current ILA methodology
ILA bridges the hardware-software boundary
  ILAs allow us to formally reason about both hardware and software
  This lets us verify properties about the interaction between an accelerator and a program
ILA maintains sequential programming abstractions
  ILAs have a single thread of control
  ILAs are deterministic: after fetching input, exactly one instruction’s decode condition holds
How do we extend ILA to model data-parallelism in accelerators?
Can we maintain the view of sequential abstractions (to ease verification)?
Notes: On point 1, mention serves as both a specification and an abstraction
Can verbally say what the savings are. “We don’t want our verifier to have to start reasoning about interleavings – it’s too expensive.”

## Slide 11: Outline
Background: Instruction Level Abstraction (ILA)
SIMD (Single Instruction, Multiple Data) Instructions
Nested SIMD Instructions, SIMD Transformations
Key Points
Related Work
Future Work

## Slide 12: Challenge example: FlexASR Accelerator
Tambe, Thierry, et al. "9.8 A 25mm 2 SoC for IoT Devices with 18ms Noise-Robust Speech-to-Text Latency via Bayesian Speech Denoising and Attention-Based Sequence-to-Sequence DNN Speech Recognition in 16nm FinFET." 2021 IEEE International Solid-State Circuits Conference (ISSCC). Vol. 64. IEEE, 2021. Image credit: https://github.com/harvard-acc/FlexASR
Notes: Already given general motivation. Stick to “challenge example” – don’t say specifically this example. Two goals: model data-parallelism, maintain sequential view.

## Slide 13: SIMD Instructions: Roadmap
An -SIMD instruction is a sequential abstraction of hardware simultaneously performing the same operation on instances of the same type of data.
Roadmap
Definition:
  instances of the same type of data
  same operation
  -SIMD instruction
  Example
Verification: maintaining a sequential abstraction
Challenge Example
…
…
Notes: Explain notation in figure

## Slide 14: instances of the same type of data
We extend our type system:
…
…
Type | Bool ¦ Bitvector(nbits) ¦ Memory(databits, addrbits) ¦ Vector(, ) ¦ Record
Example (Row/column vectors, Matrix) If , consider an ILA with variables:
Notes: Highlight the meaning of t and r in the vector, explain I’ve included the typing judgements to establish a notation. Know 3 challenges mentioned in CASES paper. Take opportunity to mention float8 is an example of custom numerics taken from FlexASR.

## Slide 15: Same operation
 | is the data atom, is the unit of state being updated
 | is the state used (read/written) in order to update Note .
 | is the input read in order to update
 | , is the decode condition of
 | , is a transition function giving
 | is the data atom, is the unit of state being updated
 | is the input read in order to update
Example (Dot product). Hardware:
where
where
, where
A data atom instruction, , describes the operation used to update a single unit of state:
…
…
 | is the data atom, is the unit of state being updated
 | is the state used (read/written) in order to update Note .
 | is the input read in order to update
 | is the data atom, is the unit of state being updated
 | is the data atom, is the unit of state being updated
 | is the data atom, is the unit of state being updated
Notes: Just like a regular ILA instruction, with well defined scope so that each instance can be defined parametrically in terms of its…

## Slide 16: -SIMD Instruction
An -SIMD instruction is a tuple where
…
…
 | is a data atom instruction
 | is the number of data atoms is being performed on
 | is a vector of disjoint instances of
 | the state map, denotes the state read or updated by the th data atom instruction
 | the input map, is an expression for the input read by the th data atom instruction
 | is a data atom instruction
Notes: We don’t

## Slide 17: Example -SIMD Instruction: Linear Transformation
Hardware: , using parallel operations.
We model this hardware operation with the SIMD instruction:
Example (Dot product). Hardware:
where
where
, where

## Slide 18: Maintaining a sequential abstraction
An -SIMD instruction corresponds to update operations in parallel.
To ensure a deterministic, sequential abstraction:
Each operation should be unaffected by other concurrent operations.
Two operations are conflicting if:
There are two concurrent accesses to the same memory location
At least one access is a write
We get a sequential abstraction by requiring update operations to be conflict-free:
Write-write safety. No operation writes a variable written by another operation.
Read-write safety. No operation reads a variable written by another operation.
Notes: Remember: A conflict is two concurrent accesses to the same memory location, at least one of which is a write

## Slide 19: Write-write safety is maintained by construction
The data atom instruction updates a single data atom:
each in is disjoint from the others write-write safety
Disjointness of is ensured by construction of an r-SIMD instruction.
Note many practical SIMD schemes in accelerators create disjoint s
  E.g. tilings, partitions, permutations (any one-to-one function from new to old indices)
  Common schemes can be integrated into the language
Notes: If design decisions are questioned, emphasize practicality over generality

## Slide 20: Read-write safety check
For a SIMD instruction ,
Compute read and written variables of :
Substitute to get read/written variables used to update ’s th data atom:
(Pairwise comparison) Verify read and written variables are disjoint for two arbitrary, different data atoms:

## Slide 21: Conflict-freedom check: SMT encoding
type // use to represent , where (, )
type // use to represent , depends on data-atom index
def lookup()
def conflictCheck(: , rdQ: , wrQ: ) =
  for each such that : // consider each written variable,
    if lookup(rdQ, ) = : continue // not read
    // else use a variable to represent the location of a conflict
  let = // is a location of read to update
  let = // is a location of written to update
  if SAT(): // for , is both read and written
      return CONFLICT: is both read and written
  return OK!
Verify:

## Slide 22: Conflict-freedom check: SMT encoding
type // use to represent , where (, )
type // use to represent , depends on data-atom index
def lookup()
def conflictCheck(: , rdQ: , wrQ: ) =
  for each such that : // consider each written variable,
    if lookup(rdQ, ) = : continue // not read
    // else use a variable to represent the location of a conflict
  let = // is a location of read to update
  let = // is a location of written to update
  if SAT(): // for , is both read and written
      return CONFLICT: is both read and written
  return OK!
Verify:

## Slide 23: Conflict-freedom check: SMT encoding
type // use to represent , where (, )
type // use to represent , depends on data-atom index
def lookup()
def conflictCheck(: , rdQ: , wrQ: ) =
  for each such that : // consider each written variable,
    if lookup(rdQ, ) = : continue // not read
    // else use a variable to represent the location of a conflict
  let = // is a location of read to update
  let = // is a location of written to update
  if SAT(): // for , is both read and written
      return CONFLICT: is both read and written
  return OK!
Verify:

## Slide 24: Conflict-freedom check: SMT encoding
type // use to represent , where (, )
type // use to represent , depends on data-atom index
def lookup()
def conflictCheck(: , rdQ: , wrQ: ) =
  for each such that : // consider each written variable,
    if lookup(rdQ, ) = : continue // not read
    // else use a variable to represent the location of a conflict
  let = // is a location of read to update
  let = // is a location of written to update
  if SAT(): // for , is both read and written
      return CONFLICT: is both read and written
  return OK!
Verify:

## Slide 25: Conflict-freedom check: SMT encoding
type // use to represent , where (, )
type // use to represent , depends on data-atom index
def lookup()
def conflictCheck(: , rdQ: , wrQ: ) =
  for each such that : // consider each written variable,
    if lookup(rdQ, ) = : continue // not read
    // else use a variable to represent the location of a conflict
  let = // is a location of read to update
  let = // is a location of written to update
  if SAT(): // for , is both read and written
      return CONFLICT: is both read and written
  return OK!
Verify:

## Slide 26: Conflict-freedom check: SMT encoding
type // use to represent , where (, )
type // use to represent , depends on data-atom index
def lookup()
def conflictCheck(: , rdQ: , wrQ: ) =
  for each such that : // consider each written variable,
    if lookup(rdQ, ) = : continue // not read
    // else use a variable to represent the location of a conflict
  let = // is a location of read to update
  let = // is a location of written to update
  if SAT(): // for , is both read and written
      return CONFLICT: is both read and written
  return OK!
Verify:

## Slide 27: Conflict-freedom check: SMT encoding
type // use to represent , where (, )
type // use to represent , depends on data-atom index
def lookup()
def conflictCheck(: , rdQ: , wrQ: ) =
  for each such that : // consider each written variable,
    if lookup(rdQ, ) = : continue // not read
    // else use a variable to represent the location of a conflict
  let = // is a location of read to update
  let = // is a location of written to update
  if SAT(): // for , is both read and written
      return CONFLICT: is both read and written
  return OK!
Verify:

## Slide 28: Summing Up SIMD Instructions
An -SIMD instruction models the same data-atom instruction being performed on instances of its data-atom.
  State/input maps describe which data is used to update which data-atom
We guarantee it is a sequential abstraction by ensuring the operations on each data-atom are conflict-free.
  Write-write conflicts are avoided by construction
  We check for read-write conflicts
2a. We can convert an -SIMD instruction to a normal instruction when useful
  Conflict-freedom any interleaving of data-atom updates is equivalent to the data-parallel operation
Notes: [TODO] “operations on” or “updates to”? As a consequence of point 2, the SIMD instruction being a sequential abstraction, we have…

## Slide 29: Challenge example: FlexASR
Notes: Already given general motivation. Can say this is the “concrete/specific” motivation.

## Slide 30: Challenge Example A: Processing Elements for LSTM
The 4 PEs divide a linear transformation into four parts, ,
Each PE has its own output buffer, guaranteeing write-write safety. ( is a state variable.)
No PE reads this output, guaranteeing read-write safety.

## Slide 31: Challenge Example B: Linear Transformation
Notes: Already given general motivation. Can say this is the “concrete/specific” motivation.

## Slide 32: Challenge Example B: Linear Transformation
Within each PE, ,
Nearly identical to the previous linear transformation example
Example (MAC). Hardware:
where
where
, where

## Slide 33: Challenge Example B: 16-Dim. Linear Transformation
Example (MAC). Hardware:
where
where
, where
Check conflict-freedom:
Read/written sets in data atom instruction:
Read/written sets in SIMD instruction:
Only potential read-write conflict is :
Ask solver: ?
UNSAT no conflicts!
Notes: Mention that here it’s a very simple check

## Slide 34: Challenge Example C: Parallel MaxPool (LayerReduction)
Notes: Already given general motivation. Can say this is the “concrete/specific” motivation.

## Slide 35: Challenge Example C: 16x Parallel MaxPool (LayerReduction)
ILA has states:
Data atom instruction is simple:
Offsets
Read/written data all here
State map not so much:
Let be the tiling:
Then
Hardware constants: .

## Slide 36: Challenge Example C: 16x Parallel MaxPool (LayerReduction)
Check conflict freedom:
Read/written sets in SIMD instruction:
Read/written sets in data atom instruction:
Ask solver: where ?
UNSAT, so no conflicts! (when )
Hardware constants: .
Notes: Note that you’re carrying the data-atom and M_S from previous slide, keep (when TGRP_SIZE, …) because it shows it’s the limits of the tiling scheme.

## Slide 37: Challenge Example C: How fast is the read-write check?
Examples A, B have trivial checks. Let’s look at C.
Solver returns UNSAT (No conflicts) in 0.29s
Example C is part of a nested loop structure:
for
  for
    for
      for :
      = max( )
Sequential in hardware
SIMD instruction,
(For demonstration) Let’s check if these loops are SIMD also!

## Slide 38: Challenge Example C: How fast is the read-write check?
Problem | Result
MaxPool over | SAT – conflict found
MaxPool over | UNSAT – no conflicts!
MaxPool over | SAT – conflict found
MaxPool over | UNSAT – no conflicts!
Problem | Result
 | SAT – conflict found
 | UNSAT – no conflicts!
 | SAT – conflict found
 | UNSAT – no conflicts!
Caveat
Timing data does not include time to find read/write sets
Opportunity
These results are from modeling the specific hardware of FlexASR, i.e. hardware constants are concretized:
Let’s keep these constants symbolic.
for
  for
    for
      for :
      = max( )

## Slide 39: Challenge Example C: How fast is the read-write check?
for
  for
    for
      for :
      = max( )
Hardware constants kept symbolic:
Models families of accelerator designs!
Checking the loop might be improved with better invariants
  Future work: modeling using CHCs
156s

## Slide 40: Challenge example: FlexASR
Modeled!

## Slide 41: Implementation: extending ILAng framework
Extension to ILAng is partially implemented:
Added support for vectors and records as syntactic sugar
Some utilities for making disjoint (write-write safety by construction)
Preliminary read-write check implemented
Further improvements:
Vectors/records should be part of expressions
Integrate read-write check with ILAng models

## Slide 42: Summary so far
How do we extend ILA to model data-parallelism in accelerators?
Use SIMD instructions to encapsulate the data-parallel portion!
Can we maintain the view of sequential abstractions (to ease verification)?
Yes, by ensuring conflict-freedom!
Next question: we have an abstraction, what can we do with it?

## Slide 43: Outline
Background: Instruction Level Abstraction (ILA)
SIMD (Single Instruction, Multiple Data) Instructions
Nested SIMD Instructions, SIMD Transformations
Key Points
Related Work
Future Work

## Slide 44: Nested SIMD Instructions
Definition of a data atom instruction:
Just showed:
  -SIMD instructions can be used like standard ILA instructions
A standard ILA instruction (that only writes to )
…
…
…
…
…
…
…
data-atoms, each is a
same operation,
Potentially different
= ,
Notes: Hardware

## Slide 45: SIMD Transformation: Flattening
Can flatten nested -SIMD instructions into an -SIMD instruction
  Write-write safety is guaranteed by disjointness of
  Read-write safety is guaranteed by conflict-freedom checks at each nesting level
Like this, other loop transformations can be implemented
  E.g. loop reordering, loop fusion
…
…
…
…
…
…
…
…
…
,

## Slide 46: Summary of Key Points
SIMD instructions allow us to
model hardware data-parallelism and
preserve a sequential view of hardware
We check conflict-freedom to ensure the sequential abstraction
This approach allows us to further raise the level of abstraction via loop transformations

## Slide 47: Related Work
Data-parallelism and loop transformations | 
Halide | Ragan-Kelley, Jonathan, et al. "Halide: a language and compiler for optimizing parallelism, locality, and recomputation in image processing pipelines." Acm Sigplan Notices 48.6 (2013): 519-530.
Verification of programs on parallel hardware | 
GPUVerify | Betts, Adam, et al. "GPUVerify: a verifier for GPU kernels." Proceedings of the ACM international conference on Object oriented programming systems languages and applications. 2012.
ILA | Huang, Bo-Yuan, et al. "Formal security verification of concurrent firmware in SoCs using instruction-level abstraction for hardware." 2018 55th ACM/ESDA/IEEE Design Automation Conference (DAC). IEEE, 2018.
 | Zhang, Hongce, et al. "ILA-MCM: Integrating Memory Consistency Models with Instruction-Level Abstractions for Heterogeneous System-on-Chip Verification." 2018 Formal Methods in Computer Aided Design (FMCAD). IEEE, 2018.

## Slide 48: Future Work
More design patterns with parallelism/SIMD
Support transformations on SIMD instructions: loop reordering, loop fusion
Other types of structured parallelism: reductions, producer-consumer
Supporting ILA-based verified compilation
ILA program fragment verification
CHC-based techniques
FlexASR func A:
instr. 1 (STR r2, 0xffff0000)
instr. 2 (LDR r3, 0xffff0010)
FlexASR func B:
instr. 3 (STR r2, 0xffffaa00)
instr. 4 (LDR r3, 0xffffaabb)
NVDLA func C:
instr. 5 (STR r4, 0xffff0100)
instr. 6 (LDR r5, 0xffff0110)
Compiler-side
ILA
Accelerator-side ILA
Notes: Can use “Supporting ILA-based verified compilation“ to lead into 3LA project